## Slide 1
10.1
Chapter 10
Error Detection and Correction
Presented by NTR
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: 1

## Slide 2
10.2
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.
Note
Notes: 2

## Slide 3
10.3
10-1 INTRODUCTION
Let us first discuss some issues related, directly or indirectly, to error detection and correction.
Types of Errors Redundancy Detection Versus Correction Forward Error Correction Versus Retransmission Coding
Modular Arithmetic
Topics discussed in this section:
Notes: 3

## Slide 4
10.4
In a single-bit error, only 1 bit in the data unit has changed.
Note
Notes: 4

## Slide 5
10.5
Figure 10.1 Single-bit error
Notes: 5

## Slide 6
10.6
A burst error means that 2 or more bits in the data unit have changed.
Note
Notes: 6

## Slide 7
10.7
Figure 10.2 Burst error of length 8
Notes: 7

## Slide 8: How to detect the errors
Error detection means to decide whether the received data is correct or not without having a copy of the original message.
To detect or correct errors, we need to send some extra bits with the data.
The extra bits are called as redundant bits.

## Slide 9: Redundancy
The central concept in error detection and correction
The redundant bits are added by the sender and removed by the receiver
Their presence helps the receiver to detect and correct corrupted bits
10.9

## Slide 10: Redundancy
10.10
To detect or correct errors, we need to send extra (redundant) bits with data.
Note
Notes: 10

## Slide 11
10.11
Figure 10.3 The structure of encoder and decoder
Notes: 11

## Slide 12: Coding
Redundancy is achieved through various coding schemes
The coding schemes are divided into two broad categories
Block coding
Convolution coding
10.12

## Slide 13
10.13
In this book, we concentrate on block codes; we leave convolution codes to advanced texts.
Note
Notes: 13

## Slide 14
10.14
Figure 10.4 XORing of two single bits or two words
Notes: 14

## Slide 15
10.15
10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords.
Error Detection Error Correction Hamming Distance
Minimum Hamming Distance
Topics discussed in this section:
Notes: 15

## Slide 16
10.16
Figure 10.5 Datawords and codewords in block coding
Notes: 16

## Slide 17
10.17
The 4B/5B block coding discussed in Chapter 4 is a good example of this type of coding. In this coding scheme, k = 4 and n = 5. As we saw, we have 2k = 16 datawords and 2n = 32 codewords. We saw that 16 out of 32 codewords are used for message transfer and the rest are either used for other purposes or unused.
Example 10.1
Notes: 17

## Slide 18: Error detection in block-coding
If the following two conditions are met, the receiver can detect a change in the original codeword.
1. The receiver has (or can find) a list of valid codewords.
2. The original codeword has changed to an invalid one.
if the codeword is corrupted during transmission but the received word still matches a valid codeword, the error remains undetected.
This type of coding can detect only single error. Two or more errors may remain undetected.

## Slide 19
10.19
Figure 10.6 Process of error detection in block coding
Notes: 19

## Slide 20
10.20
Table 10.1 A code for error detection (Example 10.2)
Notes: 20

## Slide 21
10.21
Let us assume that k = 2 and n = 3. Table 10.1 shows the list of datawords and codewords. Later, we will see how to derive a codeword from a dataword.
Assume the sender encodes the dataword 01 as 011 and
sends it to the receiver. Consider the following cases:
1. The receiver receives 011. It is a valid codeword. The receiver extracts the dataword 01 from it.
Example 10.2
Notes: 21

## Slide 22
10.22
2. The codeword is corrupted during transmission, and 111 is received. This is not a valid codeword and is discarded.
3. The codeword is corrupted during transmission, and 000 is received. This is a valid codeword. The receiver incorrectly extracts the dataword 00.
Thus two corrupted bits have made the error undetectable.
Example 10.2 (continued)
Notes: 22

## Slide 23
10.23
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.
Note
Notes: 23

## Slide 24: Error correction in block-coding
IT can be handled in two ways:
  Receiver can have the sender retransmit the entire data unit.
  The receiver can use an error-correcting code, which automatically corrects certain errors.

## Slide 25
10.25
Figure 10.7 Structure of error correction in Block Coding
Notes: 25

## Slide 26
10.26
The Hamming distance between two words is the number of differences between corresponding bits.
Note
Notes: 26

## Slide 27: Hamming distance
The Hamming distance between two strings, a and b is denoted as d(a,b). It is used for error detection or error correction when data is transmitted over computer networks.
  In order to calculate the Hamming distance between two strings, a and b, we perform their XOR operation, (a⊕ b), and then count the total number of 1s in the resultant string.

## Slide 28
10.28
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2 because
Example 10.4
2. The Hamming distance d(10101, 11110) is 3 because
Notes: 28

## Slide 29: Minimum Hamming Distance
In a set of strings of equal lengths, the minimum Hamming distance is the smallest Hamming distance between all possible pairs of strings in that set.
The number of error bits a coding scheme can detect with a minimum hamming distance of d is d-1.

## Slide 30
10.30
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Note
Notes: 30

## Slide 31
There are four different codewords which can have 6 possible pairs
(000, 011)
(000, 101)
(000, 110)
(011, 101)
(011, 110)
(101.110)
10.31

## Slide 32
10.32
Find the minimum Hamming distance of the coding scheme in Table 10.2.
Solution
We first find all the Hamming distances.
The dmin in this case is 3.
Example 10.6
Notes: 32

## Slide 33
10.33
10-4 CYCLIC CODES
Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
Cyclic Redundancy Check Hardware Implementation Polynomials Cyclic Code Analysis
Advantages of Cyclic Codes Other Cyclic Codes
Topics discussed in this section:
Notes: 33

## Slide 34
10.34
Table 10.6 A CRC code with C(7, 4)
Notes: 34

## Slide 35
10.35

## Slide 36
10.36

## Slide 37
10.37
Figure 10.15 Division in CRC encoder
Notes: 37

## Slide 38
10.38
Figure 10.16 Division in the CRC decoder for two cases
Notes: 38

## Slide 39: Cyclic Redundancy Check
We can create cyclic codes to correct errors. We discuss a subset of cyclic codes called the cyclic redundancy check (CRC), which is used in networks such as LANs and WANs.
Can detect all odd errors single bit and burst error of length equal to polynomial degree.

## Slide 40: CRC generation at sender side
Find the length of the divisor ‘L’.
Append’L-1’ bits to the original message.
Perform binary division operation.
Remainder of the division =CRC.
Message to be transmitted=Message+CRC

## Slide 41: CRC generation at Receiver side
1.Receive the transmitted Message+CRC.
2. Divide it by divisor.
3. If we found remainder error occur.
4 If there is no remainder no error in data.

## Slide 42
10.42
Figure 10.21 A polynomial to represent a binary word
Notes: 42

## Slide 43
10.43
Figure 10.22 CRC division using polynomials
Notes: 43

## Slide 44
10.44
The divisor in a cyclic code is normally called the generator polynomial
or simply the generator.
Note
Notes: 44

## Slide 45
Dataword: d(x)
Syndrome: s(x)
Codeword: c(x)
Error: e(x)
Generator: g(x)
10.45

## Slide 46
10.46
In a cyclic code,
If s(x) ≠ 0, one or more bits is corrupted.
If s(x) = 0, either
a. No bit is corrupted. or
b. Some bits are corrupted, but the decoder failed to detect them.
Note
Notes: 46

## Slide 47
10.47
In a cyclic code, those e(x) errors that are divisible by g(x) are not caught.
Note
Notes: 47

## Slide 48
10.48
If the generator has more than one term and the coefficient of x0 is 1, all single errors can be caught.
Note
Notes: 48

## Slide 49
10.49
Table 10.7 Standard polynomials
Notes: 49

## Slide 50
10.50
10-5 CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking
Idea One’s Complement Internet Checksum
Topics discussed in this section:
Notes: 50

## Slide 51: Checksum
Checksum= Check+sum
Sender side- Checksum Creation
Receiver side- Checksum Validation

## Slide 52: Checksum operation at Sender Side
Block of the original message in to “k” number of blocks with “n” bits in each block
Sum all the “k” data blocks.
Add the carry to the sum, if any.
Do 1’s complement to the sum=Checksum

## Slide 53: Checksum operation at Receiver Side
Collect all the data blocks incuding the Checksum
Sum all the data blocks and checksum
If the result is all 1’s, ACCEPT; Else, REJECT

## Slide 57
10.57
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.
Example 10.18
Notes: 57

## Slide 58
10.58
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver can add all the numbers received (including the checksum). If the result is 0, it assumes no error; otherwise, there is an error.
Example 10.19
Notes: 58

## Slide 59
10.59
How can we represent the number 21 in one’s complement arithmetic using only four bits?
Solution
The number 21 in binary is 10101 (it needs five bits). We can wrap the leftmost bit and add it to the four rightmost bits. We have (0101 + 1) = 0110 or 6.
Example 10.20
Notes: 59

## Slide 60
10.60
How can we represent the number −6 in one’s complement arithmetic using only four bits?
Solution
In one’s complement arithmetic, the negative or complement of a number is found by inverting all bits. Positive 6 is 0110; negative 6 is 1001. If we consider only unsigned numbers, this is 9. In other words, the complement of 6 is 9. Another way to find the complement of a number in one’s complement arithmetic is to subtract the number from 2n − 1 (16 − 1 in this case).
Example 10.21
Notes: 60

## Slide 61
10.61
Let us redo Exercise 10.19 using one’s complement arithmetic. Figure 10.24 shows the process at the sender and at the receiver. The sender initializes the checksum to 0 and adds all data items and the checksum (the checksum is considered as one data item and is shown in color). The result is 36. However, 36 cannot be expressed in 4 bits. The extra two bits are wrapped and added with the sum to create the wrapped sum value 6. In the figure, we have shown the details in binary. The sum is then complemented, resulting in the checksum value 9 (15 − 6 = 9). The sender now sends six data items to the receiver including the checksum 9.
Example 10.22
Notes: 61

## Slide 62
10.62
The receiver follows the same procedure as the sender. It adds all data items (including the checksum); the result is 45. The sum is wrapped and becomes 15. The wrapped sum is complemented and becomes 0. Since the value of the checksum is 0, this means that the data is not corrupted. The receiver drops the checksum and keeps the other data items. If the checksum is not zero, the entire packet is dropped.
Example 10.22 (continued)
Notes: 62

## Slide 63
10.63
Figure 10.24 Example 10.22

## Slide 64
10.64
Sender site:
1. The message is divided into 16-bit words.
2. The value of the checksum word is set to 0.
3. All words including the checksum are added using one’s complement addition.
4. The sum is complemented and becomes the checksum.
5. The checksum is sent with the data.
Note
Internet Checksum
Notes: 64

## Slide 65
10.65
Receiver site:
1. The message (including checksum) is divided into 16-bit words.
2. All words are added using one’s complement addition.
3. The sum is complemented and becomes the new checksum.
4. If the value of checksum is 0, the message is accepted; otherwise, it is rejected.
Note
Internet Checksum
Notes: 65

## Slide 66
10.66
Let us calculate the checksum for a text of 8 characters (“Forouzan”). The text needs to be divided into 2-byte (16-bit) words. We use ASCII (see Appendix A) to change each byte to a 2-digit hexadecimal number. For example, F is represented as 0x46 and o is represented as 0x6F. Figure 10.25 shows how the checksum is calculated at the sender and receiver sites. In part a of the figure, the value of partial sum for the first column is 0x36. We keep the rightmost digit (6) and insert the leftmost digit (3) as the carry in the second column. The process is repeated for each column. Note that if there is any corruption, the checksum recalculated by the receiver is not all 0s. We leave this an exercise.
Example 10.23
Notes: 66

## Slide 67
Appendix A

## Slide 68
10.68
Figure 10.25 Example 10.23
Notes: 68